## Slide 1: Spirit Level
Mission 11

## Slide 2: Pre-Mission Preparation
In this mission you will use an accelerometer to determine if something is level.
Your cell phone can detect if it is level or tilted. What other devices use some kind of sensor to determine their orientation?

## Slide 3: Mission 11: Reaction Time
How level is your desk or table?
Write some code to find out. During
this project you will build a spirit level.
Project Goals:
Display a numeric "tilt" value from the accelerometer.
Scale the raw tilt value to show 0° to 90° incline.
Replace the number display with a graphical ball simulation!

## Slide 4: Objective #1: Accel
This mission will use CodeX’s built-in accelerometer
What is an accelerometer?
Click on
Go to the Mission Log and answer the question.
Return to the digital instructions.
Go back to the Mission Log and answer the question.

## Slide 5: Mission Activity #1
DO THIS:
Close the instruction panel
Use the camera controls to zoom in
Click on the accelerometer
Create a new file named Spirit_Level

## Slide 6: Objective #2: Tilt-o-Matic
When you read the accelerometer, it returns three values, one for each axis.
The three values are enclosed in parenthesis: (x, y, z)
This type of data is called a tuple.
Other tuples:
  Color values: (red, green, blue)
  Location on a grid: (x, y)

## Slide 7: Objective #2: Tilt-o-Matic
To read the accelerometer, use this code:
val = accel.read()
A tuple is a special kind of list. You can get specific x, y or z values like items in a list:
tilt_x = val[0] # first value is at index 0 tilt_y = val[1] tilt_z = val[2]

## Slide 8: Objective #2: Tilt-o-Matic
This mission will use CodeX’s built-in accelerometer
Go to the Mission Log and answer the questions about data from the accelerometer.

## Slide 9: Mission Activity #2
DO THIS:
Read the accelerometer
Display the x value
Delay a short time to read the display
Your code could look like this:

## Slide 10: Objective #3: Scale to Degrees
The numbers you see on the display are all over the place.
We usually measure angles in degrees.
You need to convert the raw data -- numbers you see on the display -- into degrees.
This involves some complicated math -- trigonometry -- so use the code given and don’t worry about the actual math

## Slide 11: Mission Activity #3
DO THIS:
Import the math module
Add the code as shown
Change the display.print to show degrees
Run the code
  Can you get CodeX level, with 0 degrees?
Go to the Mission Log and answer the question

## Slide 12: Objective #4: Static Ball
Time to learn a little about drawing on the display
Here are the drawing functions you will use for your spirit level:

## Slide 13: Objective #4: Static Ball
Concept: The display
The CodeX LCD display is 240 pixels x 240 pixels
Each tiny pixel works JUST like the 4 RGB LED pixels at the top of the CodeX.
x in the (x, y) is the display width
y is the display height

## Slide 14: Mission Activity #4
DO THIS:
Define a value for the center of the display
Type the code to draw a line in the center
Change the display.print to drawing a circle instead

## Slide 15: Objective #5: Rolling Stone
Time to make that ball move
Use the information you have:
  Center of display
  Degrees for x
Use math to calculate the position of the circle
Use a variable for the data

## Slide 16: Mission Activity #5
DO THIS:
Define a value for the x position
Assign it the value:
  x = CENTER + degrees
Use the variable in the draw_circle() command
Run the code and tilt CodeX to see the ball move

## Slide 17: Accelisplay
During this mission you have learned about the accelerometer and the display.
Answer 3 quiz questions about the concepts.
CODEX
QUIZ

## Slide 18: Objective #6: Eraser First
Spirit Level -- final touches
Why is the ball drawing on top of itself?
Because you are not erasing it first.
Cover your tracks!
Draw a white circle to “erase” the current circle before moving to a new position and drawing a new orange circle.

## Slide 19: Mission Activity #6
DO THIS:
Define the x variable above the while loop
Draw a white circle before calculating a new x value
Run your program Does it work correctly?

## Slide 20: Post-Mission Reflection
Read the “completed mission” message and click to complete the mission
Complete the Mission 11 Log

## Slide 21: Clearing your CodeX
Go to FILE -- BROWSE FILES
Select the “Clear” file and open it
Run the program to clear the CodeX